## Slide 1
Biometric Solutions
Name of Presenter
Technical Presentation

## Slide 2
About Us
35 years of experience
In-house R&D teams
Fully-owned world-class manufacturing facilities
USA | CHINA | ISRAEL

## Slide 3: Worldwide Presence
Dallas
Israel
India
Shenzhen
Hong Kong
Colombia
Argentina
Shanghai
Beijing
Xi’an

## Slide 4: Partners

## Slide 5
9000 Biometric Series
AY-B91x0BT
AY-B92x0BT
AY-B9350
DR-9000

## Slide 6
20,000 fingerprint templates, 10,000 users
Support Wiegand 26- and 34-Bit formats
Built-in output relay for controlling a local door
RosslareBio 9000 Client/Server software
Support Rosslare BLE-ID and BLE-Admin apps (selected modules)
Face recognition (AY‑B9350)
9000 Biometric Series
General

## Slide 7
9000 Biometric Series
Compression Table
 | AY-B9120BT | AY-B9150BT | AY-B9250BT | AY-B9350
Templates | 20,000 | 20,000 | 20,000 | 20,000
Users | 10,000 | 10,000 | 10,000 | 10,000
EM | V | X | X | V
MIFARE (CSN) | X | V | V | V
BLE | V | V | V | X
Face Recognition | X | X | X | V
Snap Shot Camera | X | X | V | X
Door Relay | V | V | V | V
Multi-level Authentication | Card / FP | Card / FP | Card / FP | Card / FP / Face / Code
Notes: Multi Levels Authentication – refer to “OR” / “AND” working mode, in AND mode all levels are require, this mean the if a user using card, FP, Face and code all 4 will be need to gain access

## Slide 8
AY-B9120BT/9150BT

## Slide 9
AY-B9120 BT – Supports 125 kHz
AY-B9150 BT – Supports 13.56 MHz (MIFARE Classic)
Must use the AY-B91x0 power supply
Recommended cable – 22AWG
IP address can be set up using BLE-Admin app or RosslareBio 9000 software (LAN only)
AY-B9120BT/9150BT
General

## Slide 10
AY-B9120BT/9150BT
Terminal Description
LED
Fingerprint Sensor
RF ID Reader

## Slide 11
Power and Ethernet
AY-B9120BT/9150BT
Wiring
Ethernet RJ-45
Power Supply

## Slide 12
Wiegand
AY-B9120BT/9150BT
Wiring
DO
D1
GND
To Controller

## Slide 13
Power off the AY-B91x0BT
Connect the yellow wire (WO 1) to pink wire (WI 1)
Connect the orange wire (WO 0) to brown wire (WI 0)
Power on the AY-B91x0BT
The device is set to factory default now
AY-B9120BT/9150BT
Set to Factory Default

## Slide 14
Lock Connection – while using as Standalone
AY-B9120BT/9150BT
Wiring

## Slide 15
AY-B9250BT

## Slide 16
Support 13.56 MHz (MIFARE Classic)
On terminal display
  User ID
  Time
  Function keys
4 buttons for configuration
Recommended cable – 22AWG
Built-in camera for access event snap shots
AY-B9250BT
General

## Slide 17
AY-B9250BT
Terminal Description
LCD Display
Camera
Function Buttons
LED
Fingerprint Sensor
RF ID Reader

## Slide 18
AY-B9250BT
Terminal Screen Description
Network Status
Door Status
Function Key
Fire Alarm
Time / Date

## Slide 19
Power and Ethernet
AY-B9250BT
Wiring
Ethernet RJ-45
Power Supply

## Slide 20
Wiegand
AY-B9250BT
Wiring
DO
D1
GND
10
11
To Controller

## Slide 21
Power off the AY-B9250BT
On the back side of the terminal set the 2 dipswitches to ON:
Power on the AY-B9250BT
After the terminal completely boots, press [F1] longer to enter the menu with the buzzer sound “Ppiririk”.
AY-B9250BT
Set to Factory Default

## Slide 22
AY-B9350BT

## Slide 23
Support 13.56 MHz (MIFARE Classic) and 125 kHz (EM)
Touch screen
Face recognition using 2 cameras
Recommended cable – 22AWG (max 15 meters from power supply)
AY-B9350
General

## Slide 24
AY-B9350
Terminal Description
IR LEDs
RF ID Reader
Touch Screen
Light Sensor
Fingerprint Sensor
Dual Camera Face Recognition

## Slide 25
AY-B9350
Terminal Screen Description
Network Status
Door Status
T&A selector
Warnings
Time / Date
Camera Video
Face Detection
Input ID

## Slide 26
Power and Ethernet
AY-B9350
Wiring
Power Supply
Ethernet RJ-45

## Slide 27
Wiegand
AY-B9350
Wiring
DO
GND
D1
Wiegand Cable
To Controller

## Slide 28
AY-B9350
Installation – Recommended Height
Terminal mounting plate (recommended)

## Slide 29
Install the device indoors
Do not install under an incandescent light
Do not install where there is direct sunlight or counter-light
AY-B9350
Installation – Limitations

## Slide 30
DR-9000

## Slide 31
Desktop fingerprint enrollment device
Supports RosslareBio 9000 management SW
USB 2.0 connectivity
Win OS support
Scratch-proof surface
Crystal clear finger scan images
Driver installation needed
DR-9000
General

## Slide 32
Correct fingerprint input method
Make sure that the fingerprint is clear and not wounded
9000 Biometric Series
Fingerprint Enrollment

## Slide 33
RosslareBio 9000 – Management Software

## Slide 34
Supports multiple terminals
Supports any Windows based OS
Supports DR-9000 enrollment device (DR-9000)
User management
Fingerprint management
Time and Attendance
Time zones
MS-SQL DB (for SQL Server settings, please see SQL Servers setting section on this presentation)
RosslareBio 9000
General

## Slide 35
Run the installation software
RosslareBio 9000
Installation
Click Next

## Slide 36
RosslareBio 9000
Installation
2. Click Next
1. Accept

## Slide 37
Enter the details
Serial Number - 010301-BDB9EED54D8C0A0A-D1A759391E116FD5 for all installation
RosslareBio 9000
Installation
4. Click Next
1. User Name
2. Company Name
3. Serial number

## Slide 38
Confirm installation folder
RosslareBio 9000
Installation
Click Next

## Slide 39
Select installation type
RosslareBio 9000
Installation
Click Next
Local server and client
Client only – connected to remote server

## Slide 40
Click Install
RosslareBio 9000
Installation as Server
Click Install

## Slide 41
Set SQL connection
For SQL Server pre-setting, see SQL server setting at the end of this presentation
RosslareBio 9000
Installation as Server
Click Next
SQL Server Details
Authentication Details – Must use sa
Click Search for Path
Notes: SQL server Details:
  Name from list or IP (localhost can be used)
  For AxTraxNG Default DB use
    IP – localhost
    Instance - VERITRAX
SQL Authentication details – Must use SA

## Slide 42
Set Server connection
RosslareBio 9000
Installation as Server
Click OK
Client Connection IP
Terminals Connection IP
Client Connection port
Terminals Connection port
Terminals per Server
Remote Clients
Notes: Max Terminal – not more than 1000 per server
Max Client –not more than 50 per server

## Slide 43
Complete installation
RosslareBio 9000
Installation
Click Finish

## Slide 44
RosslareBio 9000
First Run Setting
Click Next
FP and ID
Card Reading setting
Security Level
Encryption Type
Time & Attendance
Remote Clients
Notes: Default Values cannot be modified after it been changed!
Card Reading setting recommended to use Wiegand 22bit and unified
Security level – for server authentication mode – only when need to use server DB for authentication – default mode is terminal DB.
Default Time and Attendance mode is “not use” to enable un mark the not use.

## Slide 45
RosslareBio 9000
First Run Setting
Click OK
User Information
Authentication
Notes: User Information: this is the first user\ operator in the system and will be use for login the SW till more user with “Master” rights are set.
  User ID – Should not be all “0” and ID following the setting on prev. section is allowed
  User Name – any Text
  Privilege – user rights – for first user should be Master
  Position – Text
  Personal Registration Number – usually ID number
  Description – Text
Authentication
  Authentication Type FP/ PW/ Card – for first user keep it to password and Numbers only
  User password

## Slide 46
Open the SQL Server Configuration Manager.
Brows to “Protocols for XXXXX (default VERITRAX)
RosslareBio 9000
SQL Server Setting
Instance protocols

## Slide 47
Double-click on “Named Pipe”
Under protocol Tab, make sure “Enabled” is set to ”Yes”
RosslareBio 9000
SQL Server Setting

## Slide 48
Double-click on “TCP/IP”
Under protocol Tab, make sure “Enabled” is set to ”Yes”
RosslareBio 9000
SQL Server Setting

## Slide 49
On IP Addresses tab, make sure all listed IPs are Active, Enabled, and IP address is set to PC IP Address
Click Apply
RosslareBio 9000
SQL Server Setting

## Slide 50
Go to SQL Server Services topic
RosslareBio 9000
SQL Server Setting
Server Services

## Slide 51
Make sure SQL Server Browser is Running
RosslareBio 9000
SQL Server Setting

## Slide 52
RosslareBio 9000
SQL Server Setting
Select SQL Server (Instance Name)
Click Restart Server button
Restart Server

## Slide 53
Ing. Mariano Bianchi – Techincal support manager.
+54.9.11.5728.9751
Mariano.Bianchi@rosslaresecurity.com